## Slide 1
Chapter 5 x86 Assembly Language
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
1

## Slide 2
These slides are meant to be used along with the book: Computer Organisation and Architecture, Smruti Ranjan Sarangi, McGrawHill 2015
Visit: http://www.cse.iitd.ernet.in/~srsarangi/archbooksoft.html

## Slide 3: Overview of the x86 ISA
It is not one ISA
  It is a family of ISAs
The great-grandfather in the family
  Is the 8-bit 8080 microprocessor used in the mid-seventies
The grandfather is the 16-bit 8086 microprocessor released in 1978
The parents are the 32 bit processors : 80386, 80486, Pentium, and Pentium IV
The current generation of processors are 64 bit processors : Intel Core i3, i5, i7

## Slide 4: Main Features of the x86 ISA
It is a CISC ISA
Has more than 300+ instructions
Instructions can have a source/ destination memory operand
Uses the stack for passing arguments, and return addresses
Uses segmented memory

## Slide 5: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 6: View of Registers
Modern Intel machines are still ISA compatible with the arcane 16 bit 8086 processor
In fact, due to market requirements, a 64 bit processor needs to be ISA compatible with all 32 bit, and 16 bit ISAs
What do we do with registers?
Do we define a new set of registers for each type of x86 ISA? ANSWER : NO

## Slide 7: View of Registers – II
Consider the 16 bit x86 ISA – It has 8 registers: ax, bx, cx, dx, sp, bp, si, di
Should we keep the old registers, and create a new set of registers in a 32 bit processor?
NO – Widen the 16 bit registers to 32 bits.
If the processor is running a 16 bit program, then it uses the lower 16 bits of every 32 bit register.

## Slide 8: View of Registers – III
The 64 bit ISA has
8 extra registers
r8 - r15
8 registers
64, 32, 16
bit variants
eax
ebx
ecx
edx
esp
ebp
esi
edi
ax
bx
cx
dx
sp
bp
si
di
rax
rbx
rcx
rdx
rsp
rbp
rsi
rdi
r8
r9
r15
64 bits
32 bits
16 bits

## Slide 9: x86 can even Support 8 bit Registers
For the first four 16 bit registers
  The lower 8 bits are represented by : al, bl, cl, dl
  The upper 8 bits are represented by : ah, bh, ch, dh
ax
bx
cx
dx
ah
al
bh
bl
ch
dh
cl
dl

## Slide 10: x86 Flags Registers and PC
Similar to the SimpleRisc flags register
It has 16 bit, 32 bit, and 64 bit variants
The PC is known as IP (instruction pointer)
Fields in the flags register
eflags
eip
flags
ip
rflags
rip
64 bits
32 bits
16 bits
Field
Condition
Semantics
OF
Overflow
Set on an overflow
CF
Carry flag
Set on a carry or borrow
ZF
Zero flag
Set when the result is a 0,or the
comparison leads to an equality
SF
Sign flag
Sign bit of the result

## Slide 11: Floating-point Registers
x86 has 8 (80 bit) floating-point registers
  st0 – st7
  They are also arranged as a stack
  st0 is the top of the stack
  We can perform both register operations, as well as stack operations
st0
st1
st5
st4
st0
st0
st2
st3
st6
st7
FP register
stack

## Slide 12: View of Memory
x86 follows a segmented memory model
  Each address in x86 is actually an offset from the start of the segment.
  For example, an instruction address is an offset in the code segment
  The starting address of the code segment is maintained in a code segment (CS) register
memory
CS Register
Address
Conceptual View

## Slide 13: Segmentation in x86
x86 has 6 different segment registers
  Each register is 16 bits wide
  Code segment (cs), data segment (ds), stack segment (ss), extra segment (es), extra segment 1 (fs), extra segment 2 (gs)
cs
ss
ds
es
gs
fs
16 bit segment registers

## Slide 14: Segmented vs Linear Memory Model
In a linear memory model (e.g. SimpleRisc, ARM) the address specified in the instruction is sent to the memory system
  There are no segment registers
What are the advantages of a segmented memory model?
  The contents of the segment registers can be changed by the operating system at runtime.
  Can map the text section(code) to another part of memory, or in principle to other devices also (discussed in Chapter 10)
  Stores cannot modify the instructions in the text section. REASON : Stores use the data segment, and instructions use the code segment

## Slide 15: How does Segmentation Work
The segment registers nowadays contain an offset into a segment descriptor table
  Because, 16 bits are not sufficient to store a memory address
Modern x86 processors have two kinds of segment descriptor tables
  LDT (Local Descriptor Table), 1 per process, typically not used nowadays
  GDT (Global Descriptor Table), contains 8191 entries
  Each entry in these tables contains the starting address of the segment

## Slide 16: Segment Descriptor Cache
Every memory access needs to access the GDT or LDT : VERY SLOW
Use a segment descriptor cache (SDC) at each processor that stores a copy of the relevant entries in the GDT
  Lookup the SDC first
  If an entry is not there, send a request to the GDT
  Quick, fast, and efficient

## Slide 17: Memory Addressing Mode
x86 supports a base, a scaled index and an offset (known as the displacement)
Each of the fields is optional

## Slide 18: Examples of Addressing Modes
x86 supports memory direct addressing
The address can just be the index
It can be a combination of the base, scaled index, and displacement
Memory operand
Value of the address
(in register transfer notation)
Addressing mode
[eax]
eax
register-indirect
[eax + ecx*2]
eax + 2 * ecx
base-scaled-index
[eax + ecx*2 - 32]
eax + 2* ecx - 32
base-scaled-index-offset
[edx - 12]
edx - 12
base-offset
[edx*2]
edx * 2
scaled-index
[0xFFE13342]
0xFFE13342
memory-direct

## Slide 19: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 20: Basic x86 Assembly
We shall use the NASM assembler in this book
  Available at : http://www.nasm.us
Generic structure of an assembly statement
  <label> : <assembly instruction> ; <comment>
  Comments are preceded by a ;
x86 assembly instructions
  Typically in the 1 and 2 address format
  2 address format : <instruction> <operand 1> <operand 2>
  <operand 1> is typically both the source and destination

## Slide 21: Basic x86 Assembly – II
Rules for operands (for most instructions)
  Both the operands can be a register
  At most one of them can be an immediate
  At most one of them can be a memory location
  A memory operand is encapsulated in []
Rules for immediates
  The size of an immediate is equal to the size of the memory address
  For example, for a 32 bit machine, the maximum size of an immediate is 32 bits

## Slide 22: Basic x86 Assembly – III
We shall use the 32 bit flavour of x86 in this book
  Readers can seamlessly write 16 bit x86 programs
  Simply use the registers : ax, bx, cx, dx, sp, bp, si, di
  Readers can also write 64 bit programs by using the registers : rax, rbx, rcx, rdx, rsp, rbp, rsi, rdi, and r8 – r15

## Slide 23: The mov instruction
Extremely versatile instruction
  Can be used to load an immediate
  Load and store values to memory
  Move values between registers
Example
  mov ebx, [esp – eax*4 - 12]
Semantics
Example
Explanation
mov (reg/mem), (reg/mem/imm)
mov eax, ebx
eax ← ebx

## Slide 24: movsx and movzx instructions
The regular mov instruction assumes that the source and destination have the same size
The movsx and movzx instructions replace the MSB bits by the sign bit, or zeros respectively
Semantics
Example
Explanation
movsx reg, (reg/mem)
movsx eax,bx
eax ← sign extend(bx), the second
operand is either 8 or 16 bits
movzx reg, (reg/mem)
movsx eax,bx
eax ← zero extend(bx), the second
operand is either 8 or 16 bits

## Slide 25: Exchange Instruction
Exchanges the contents of <operand 1> and <operand 2>
Semantics
Example
Explanation
xchg (reg/mem), (reg/mem)
xchg eax, [eax + edi]
swap the contents of eax
and [eax + edi]

## Slide 26: Stack push and pop Instructions
An x86 processor is aware of the stack
It is aware that the stack pointer is stored in the register, esp
The push instruction decrements the stack pointer
The pop instruction increments the stack pointer and returns the contents at the top of the stack
Semantics
Example
Explanation
push (reg/mem/imm)
push ecx
temp ← ecx; esp ← esp - 4; [esp] ← temp
pop (reg/mem)
pop ecx
temp ← [esp]; esp ← esp + 4; ecx ← temp

## Slide 27: Specifying Memory Operand Sizes
The processor knows the size of a register operand from its name
  eax is a 32 bit operand
  ax is a 16 bit operand
What about memory operands ?
  push [eax] → How many bytes need to be pushed ?
  Solution : Use a modifier
  push dword [eax] ; pushes 32 bits
  Similarly, we need to use modifiers for other instructions such as pop (when the number of bytes to be transferred are not known)

## Slide 28: Modifiers
Modifier
Size
byte
8 bits
word
16 bits
dword
32 bits
qword
64 bits
What is the value of ebx in this code snippet?
mov eax, 10
mov [esp], eax
push dword [esp]
mov ebx, [esp]
Answer: 10

## Slide 29: ALU Instructions
All of these are 2 operand instructions
The first operand is both the source and destination
Example : Add registers eax, and ebx. Save the result in ecx
  add eax, ebx
  mov ecx, eax
Semantics
Example
Explanation
add (reg/mem), (reg/mem/imm)
add eax, ebx
eax ← eax + ebx
sub (reg/mem), (reg/mem/imm)
sub eax, ebx
eax ← eax - ebx
adc (reg/mem), (reg/mem/imm)
adc eax, ebx
eax ← eax + ebx + (carry bit)
sbb (reg/mem), (reg/mem/imm)
sbb eax, ebx
eax ← eax - ebx - (carry bit)

## Slide 30: Single Operand ALU Instructions
Semantics
Example
Explanation
inc (reg/mem)
inc edx
edx ← edx + 1
dec (reg/mem)
dec edx
edx ← edx - 1
neg (reg/mem)
neg edx
edx ← -1 * edx
Write an x86 assembly code snippet to compute: eax = -1 * (eax + 1).
Answer:
inc eax
neg eax

## Slide 31: Compare Instruction
Similar to SimpleRisc, the cmp instruction sets the flags
Semantics
Example
Explanation
cmp (reg/mem), (reg/mem/imm)
cmp eax, [ebx+4]
compare the values in eax, and
[ebx+4], and set the flags
cmp (reg/mem), (reg/mem/imm)
cmp ecx, 10
compare the content of ecx with
10, and set the flags

## Slide 32: Multiplication and Division Instructions
The imul instruction has three variants
  1 operand form → Saves the 64 bit result in edx:eax
  eax contains the lower 32 bits, and edx contains the upper 32 bits
Semantics
Example
Explanation
imul (reg/mem)
imul reg, (reg/mem)
imul reg, (reg/mem), imm
idiv (reg/mem)
imul ecx
imul ecx, [eax + 4]
imul ecx, [eax + 4], 5
idiv ebx
edx:eax ← eax * ecx
ecx ← ecx * [eax + 4]
ecx ← [eax + 4] * 5
Divide (edx:eax) by the contents
of ebx; eax contains the quotient,
and edx contains the remainder.

## Slide 33: imul Instruction - II
2 operand form
  The first operand (source and destination) has to be a register
  The second operand can either be a register or memory location
Semantics
Example
Explanation
imul (reg/mem)
imul reg, (reg/mem)
imul reg, (reg/mem), imm
idiv (reg/mem)
imul ecx
imul ecx, [eax + 4]
imul ecx, [eax + 4], 5
idiv ebx
edx:eax ← eax * ecx
ecx ← ecx * [eax + 4]
ecx ← [eax + 4] * 5
Divide (edx:eax) by the contents
of ebx; eax contains the quotient,
and edx contains the remainder.

## Slide 34: imul Instruction - III
3 operand form
  First operand (destination) → register
  First source operand (register or memory)
  Second source operand (immediate)
Semantics
Example
Explanation
imul (reg/mem)
imul reg, (reg/mem)
imul reg, (reg/mem), imm
idiv (reg/mem)
imul ecx
imul ecx, [eax + 4]
imul ecx, [eax + 4], 5
idiv ebx
edx:eax ← eax * ecx
ecx ← ecx * [eax + 4]
ecx ← [eax + 4] * 5
Divide (edx:eax) by the contents
of ebx; eax contains the quotient,
and edx contains the remainder.

## Slide 35: idiv Instruction
Takes a single operand (register or memory)
  Dividend is contained in edx:eax
    edx contains the upper 32 bits
    eax contains the lower 32 bits
  The input operand contains the divisor
    eax contains the quotient
    edx contains the remainder
    While dividing by a negative number (set edx to -1 for sign extension)
Semantics
Example
Explanation
idiv (reg/mem)
idiv ebx
Divide (edx:eax) by the contents
of ebx; eax contains the quotient,
and edx contains the remainder.

## Slide 36: Example
Write an assembly code snippet to divide -50 by 3. Save the quotient in
eax, and remainder in edx.
Answer:
mov edx, -1
mov eax, -50
mov ebx, 3
idiv ebx
At the end eax contains -16, and edx contains -2.

## Slide 37: Logical Instructions
and, or, and xor are standard 2 operand ALU instructions where the first operand is also the destination
The not instruction is a 1 operand instruction
Semantics
Example
Explanation
and (reg/mem), (reg/mem/imm)
or (reg/mem), (reg/mem/imm)
xor (reg/mem), (reg/mem/imm)
not (reg/mem)
and eax, ebx
or eax, ebx
xor eax, ebx
not eax
eax ← eax AND ebx
eax ← eax OR ebx
eax ← eax XOR ebx
eax ← ∼ eax

## Slide 38: Shift Instructions
sar (shift arithmetic right)
shr (shift logical right)
sal/shl (shift left)
The second operand(shift amount) needs to be an immediate
Semantics
Example
Explanation
sar (reg/mem), imm
shr (reg/mem), imm
sal/shl (reg/mem), imm
sar eax, 3
shr eax, 3
sal eax, 2
eax ← eax >> 3
eax ← eax >>> 3
eax ← eax << 2

## Slide 39: Example
What is the output of this code snippet?
mov eax, 0xdeadfeed
sar eax, 4
Answer: 0xfdeadfee
What is the output of this code snippet?
mov eax, 0xdeadfeed
shr eax, 4
Answer: 0xdeadfee

## Slide 40: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 41: Simple Branch Instructions
jmp is a simple unconditional branch instruction
The conditional branches are of the form : j<condcode> such as jeq, jne
Semantics
Example
Explanation
jmp < label >
j< condcode >
jmp .foo
j< condcode > .foo
jump to .foo
jump to .foo if the < condcode > condition
is satisfied

## Slide 42: Condition Codes in x86
Condition code
Meaning
o
Overflow
No overflow
Below (unsigned less than)
Not below (unsigned greater than or equal to)
Equal or zero
Not equal or not zero
Below or equal (unsigned less than or equal)
Sign bit is 1 (negative)
Sign bit is 0 (0 or positive)
Less than (signed less than)
Less than or equal (signed)
Greater than (signed)
Greater than or equal (signed)
no
b
nb
e/z
ne/nz
be
s
ns
l
le
g
ge

## Slide 43: Example : Test if a number in eax is prime. Put the result in eax
x86 assembly code
mov ebx, 2 ; starting index
mov ecx, eax ; ecx contains the original number
.loop:
mov edx, 0 ; required for correct division
idiv ebx
cmp edx, 0 ; compare the remainder
je .notprime ; number is composite
inc ebx
mov eax, ecx ; set the value of eax again
cmp ebx, eax ; compare the index and the number
jl .loop
; end of the loop
mov eax, 1 ; number is prime
jmp .exit ; exit
.notprime:
mov eax, 0
.exit:

## Slide 44: Function Call and Return Instructions
The call instruction jumps to the <label>, and pushes the return address on the stack
Pops the stack top (assume it contains the return address)
Semantics
Example
Explanation
call < label >
ret
call .foo
ret
Push the return address on the stack.
Jump to the label .foo.
Return to the address saved on the top
of the stack, and pop the entry

## Slide 45: What does a typical function do ?
Extracts the arguments from the stack
Creates space on the stack to store the activation block
Spills some registers (if required)
Calls other functions
Does some processing
Restores the stack pointer
Returns

## Slide 46
Write a recursive function to compute the factorial of a number (≥ 1) stored in eax. Save the result in ebx.
Answer:
x86 assembly code
factorial:
mov ebx, 1 ; default return value
cmp eax, 1 ; compare num (input) with 1
jz .return ; return if input is equal to 1
; recursive step
push eax ; save input on the stack
dec eax ; num--
call factorial ; recursive call
pop eax ; retrieve input
imul ebx, eax ; prod = prod * num
.return:
ret ; return
Example of a Recursive Function

## Slide 47: Implementing a Function
Using push and pop instructions is fine for small functions
For large functions that have a lot of internal variables, it might be necessary to push and pop a lot of values from the stack
For languages like C++ that dynamically declare local variables, it might be difficult to keep track of the size of the activation block.
x86 processors thus save the starting value of esp in the ebp register. At the end they set esp to ebp.

## Slide 48: Recursive function for factorial : without push/pop instructions
x86 assembly code
factorial:
mov eax, [esp+4]; get the value of eax from the stack
push ebp ; *** save ebp
mov ebp, esp ; *** save the stack pointer
mov ebx, 1 ; default return value
cmp eax, 1 ; compare num (input) with 1
jz .return ; return if input is equal
; recursive step
sub esp, 8 ; create space on the stack
mov [esp+4], eax ; save input on the stack
dec eax ; num--
mov [esp], eax ; push the argument
call factorial ; recursive call
mov eax, [esp+4] ; retrieve input
imul ebx, eax ; prod = prod * num
.return:
mov esp, ebp ; *** restore the stack pointer
pop ebp ; *** restore ebp
ret ; return

## Slide 49: Enter and Leave Instructions
push ebp ; mov ebp, esp ; sub esp, <stack size> is a standard sequence of operations
  The enter instruction does all the three operations
mov esp, ebp ; pop ebp
  Standard sequence at the end of a function
  Both the operations are done by the leave instruction
Semantics
Example
Explanation
enter imm, 0
leave
enter 32, 0
leave
push ebp (push the value of ebp on the
stack); mov ebp, esp (save the stack
pointer in ebp); esp ← esp - 32
mov esp, ebp (restore the value of esp);
pop ebp (restore the value of ebp)

## Slide 50: Example with enter and leave
x86 assembly code
factorial:
mov eax, [esp+4] ; read the argument
enter 8, 0 ; *** save ebp and esp
mov ebx, 1 ; default return value
cmp eax, 1 ; compare num (input) with 1
jz .return ; return if input is equal to 1
; recursive step
mov [esp+4], eax ; save input on the stack
dec eax ; num--
mov [esp], eax ; push the argument
call factorial ; recursive call
mov eax, [esp+4] ; retrieve input
imul ebx, eax ; prod = prod * num
.return:
leave ; *** load esp and ebp
ret ; return

## Slide 51: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 52: Advanced Memory Instructions
These instructions are useful in moving a large sequence of bytes from one location to another
Also known as string instructions
They make special use of the edi and esi registers
  edi contains the default destination
  esi contains the default source

## Slide 53: The lea instruction
The lea (load effective address) inst. is used to load an address in to the edi and esi registers
  In general, lea can be used to load an address in to any register
lea ebx, [ecx + edx*2 + 16]
  ebx ← ecx + 2 * edx + 16

## Slide 54: stosd instruction
The stosd instruction does not have any operands
  It saves the value in eax to [edi] (memory location in edi)
  If the value of the DF flag in the flags register is 1
    edi ← edi – 4
  If the value in the DF flag in the flags register is 0
    edi ← edi + 4
It is a post-indexed addressing mode

## Slide 55: lodsd instruction
The lodsd instruction does not have any operands
  It saves the value in [esi] to eax (memory location in esi)
  If the value of the DF flag in the flags register is 1
    esi ← esi – 4
  If the value in the DF flag in the flags register is 0
    esi ← esi + 4
It is a post-indexed addressing mode

## Slide 56: Summary of Memory Instructions
movsd : [edi] ← [esi]
  Auto increments esi, and edi based on the DF flag
std : Sets the DF flag to 1
cld : Sets the DF flag to 0
Semantics
Example
Explanation
lea reg, mem
stos(b/w/d/q)
lods(b/w/d/q)
movs(b/w/d/q)
std
cld
lea ebx, [esi + edi*2 + 10]
stosd
lodsd
movsd
std
cld
ebx ← esi + edi*2 + 10
[edi] ← eax; edi ← edi + 4 * (−1)DF
eax ← [esi]; esi ← esi + 4 * (−1)DF
[edi] ← [esi] ; esi ← esi + 4 * (−1)DF
edi ← edi + 4 * (−1)DF
DF ← 1
DF ← 0
DF → Direction Flag

## Slide 57
What is the value of eax after executing this code snippet?
Answer: The movsd instruction transfer 4 bytes from the memory address
specified in esi to the memory address specified in edi. Since we write
192 to the memory address specified in esi, we shall read back the same
value in the last line.
mov dword [esp+4], 192
lea esi, [esp+4]
lea edi, [esp+8]
movsd
mov eax, [esp+8]

## Slide 58: Power of String Instructions
Copy a 10 element array
  Starting address of source array in esi
  Starting address of destination array in edi
cld ; DF = 0
mov ebx, 0 ; initialisation of the loop index
.loop:
movsd ; [edi] <-- [esi]
inc ebx ; increment the index
cmp ebx, 10 ; loop condition
jne .loop

## Slide 59: The rep prefix
Repeats a given instruction n times
  n is the value stored in ecx
Semantics
Example
Explanation
rep inst
rep movsd
val ← ecx; Execute the movsd instruction
val times; ecx ← 0
cld ; DF = 0
mov ecx, 10 ; Set the count to 10
rep movsd ; Execute movsd 10 times

## Slide 60: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 61: FP Machine Model
There is no direct connection between integer and FP registers
They can only communicate through memory
No way to load floating-point immediates directly
Memory
Integer
registers
FP
registers
Constants

## Slide 62: FP Load Instructions
The fld instruction pushes the value of the first operand (register/mem) to the FP stack
The fild instruction pushes an integer stored in memory to the FP stack
Semantics
Example
Explanation
fld mem
fld reg
fild mem
fld dword [eax]
fld st1
fild dword [eax]
Pushes an FP number stored in [eax] to
the FP stack
Pushes the contents of st1 to the top of
the stack
Pushes an integer stored in [eax] to the
FP stack after converting it to a 32 bit
floating point number

## Slide 63: Assembler Directives
There are two ways to load an FP immediate
  Store its hex representation to memory, and use the fld instruction to bring the value to a FP register.
  Use an assembler directive to store the immediate as a constant before the program starts. Then use the fld instruction to transfer the value to the FP stack.
In NASM :
Declares a 32 bit floating-point constant : 2.392 in the data section
section .data
num: dd 2.392

## Slide 64: Assembler Directives – II
Furthermore, the assembler associates the label num with the memory address that saves 2.392
In the assembly program, we need to write:
  fld dword [num]
With this method, we do not have to save the hex (binary) representation of a FP number. The assembler will automatically do it for us.

## Slide 65: FP Exchange
Exchanges the contents of two floating point registers
st0 is always one of the FP registers
Semantics
Example
Explanation
fxch reg
fxch st3
Exchange the contents of st0 and st3
fxch
fxch
Exchange the contents of st0 and st1

## Slide 66: FP Store Instruction
The fst instruction saves the value of st0 to memory
The fist instruction converts the FP value to an integer, and than saves it in memory.
With the 'p' suffix, the inst. also pops the FP stack
Semantics
Example
Explanation
fst mem
fst reg
fstp mem
fist mem
fistp mem
fst dword [eax]
fst st4
fstp dword [eax]
fist dword [eax]
fistp dword [eax]
[eax] ← st0
st4 ← st0
[eax] ← st0; pop the FP stack
[eax] ← int(st0)
[eax] ← int(st0); pop the FP stack

## Slide 67: Example
A 32 bit floating point number is loaded in st0. Convert it to an integer and save its value in eax.
Answer:
fist dword[esp+4] ; save st0 to [esp+4]
mov eax, [esp+4]

## Slide 68: Variants of the FP add instruction
fadd adds two FP numbers
faddp additionally pops the stack
fiadd adds an integer in the first memory operand to st0
Semantics
Example
Explanation
fadd mem
fadd reg, reg
faddp reg, reg
fiadd mem
fadd dword [eax]
fadd st0, st1
faddp st1, st0
fiadd dword [eax]
st0 ← st0 + [eax]
st0 ← st0 + st1 (one of the registers has
to be st0)
st1 ← st0 + st1; pop the FP stack
st0 ← st0 + float([eax])
fadd reg | fadd st1 | st0 ← st0 + st1
NASM
specific

## Slide 69: Subtraction, Multiplication, Division
fsub, fmul, fdiv have exactly the same form (variants) as the fadd instruction
Semantics
Example
Explanation
fsub mem
fmul mem
fdiv mem
fsub dword [eax]
fmul dword [eax]
fdiv dword [eax]
st0 ← st0 - [eax]
st0 ← st0 * [eax]
st0 ← st0 / [eax]

## Slide 70
Example: Arithmetic Mean
Compute the arithmetic mean of two integers stored in eax and ebx. Save the result (in 64 bits) in esp+4. Assume that the memory address, two, contains the constant 2.
Answer:
; load the inputs to the FP stack
mov [esp], eax
mov [esp+4], ebx
fild dword [esp]
fild dword [esp+4]
fadd st0, st1 ; compute the sum
fdiv dword [two] ; arithmetic mean
fstp qword [esp+4] ; save the result to [esp+4]
; used the qword identifier
; for specifying 64 bits

## Slide 71: Instructions for Special Functions
Semantics
Example
Explanation
fabs
fsqrt
fcos
fsin
fabs
fsqrt
fcos
fsin
st0 ← |st0|
st0 ← √st0
st0 ← cos(st0)
st0 ← sin(st0)

## Slide 72
Example: Geometric Mean
Compute the geometric mean of two integers stored in eax and ebx. Save the result (in 64 bits) in esp+4.
Answer:
; load the inputs to the FP stack
mov [esp], eax
mov [esp+4], ebx
fild dword [esp]
fild dword [esp+4]
fmul st0, st1 ; compute the product
fsqrt ; geometric mean
fstp qword [esp+4] ; save the result to [esp+4]
; used the qword identifier
; for specifying 64 bits

## Slide 73: Compare Instructions
The fcomi instruction compares the values of two FP registers and sets the flags
NOTE : It sets the flags for unsigned comparison
Semantics
Example
Explanation
fcomi reg, reg
fcomip reg, reg
fcomi st0, st1
fcomi st0, st1
compare st0 and st1, and set the eflags
register (first register has to be st0)
compare st0 and st1, and set the eflags
register; pop the FP stack

## Slide 74: Example
Compare sin(2θ) and 2sin(θ)cos(θ). Verify that they have the same value for any given value of θ. Assume that θ is stored in the data section at the label theta, and the threshold for floating point comparison is stored at label threshold. Save the result in eax (1 if equal, and 0 if unequal).
Answer:
; compute sin(2*theta), and save in [esp]
fld dword [theta]
fadd st0, st0 ; st0 = theta + theta
fsin
fstp dword [esp] ; store the value
; compute (2*sin(theta)*cos(theta))
fld dword [theta]
fst st1 ; st1 = st0 = theta
fsin ; st0 = sin(theta)
fxch ; swap st0 and st1 (st1=sin(theta))
fcos ; st0 = cos(theta)
fmul st0, st1 ; st0 = sin(theta) * cos (theta)
fadd st0, st0 ; st0 = st0 + st0

## Slide 75: Example – II
; compute the modulus of the difference
fld dword [esp] ; load (sin(2*theta))
fsub st0, st1 ; st0 = sin(2*theta)- 2*sin(theta)cos(theta)
fabs
; compare
fld dword [threshold]
fcomi st0, st1 ; compare
ja .equal ; threshold > difference (a for above)
mov eax, 0 ; else not equal
jmp .exit
.equal:
mov eax, 1 ; values are equal
.exit:

## Slide 76: Stack Cleanup Instructions
Semantics
Example
Explanation
ffree reg
finit
ffree st4
finit
Free st4
Reset the status of the FP unit including
the FP stack and registers

## Slide 77: Outline
x86 Machine Model
Simple Integer Instructions
Branch Instructions
Advanced Memory Instructions
Floating Point Instructions
Encoding the x86 ISA

## Slide 78: Overview of Instruction Encoding
The 1-4 byte prefix specifies an optional prefix
  Examples :
  Can be used to specify the rep prefix
  The lock prefix is used to specify that an instruction executes atomically in a multiprocessor system
Prefix
1-4 bytes
(optional)
Opcode
1-3 bytes
ModR/M
1 byte
(optional)
SIB
1 byte
(optional)
Displacement
1/2/4 bytes
(optional)
Immediate
1/2/4 bytes
(optional)

## Slide 79: The ModR/M Byte
Determines the addressing modes of the operands
Mod bits : (addressing mode of one of the operands)
  00 → Register indirect addressing mode
  01 → Indirect addressing mode with 1 byte displacement
  10 → Indirect addressing mode with 4 byte displacement
  11 → Register direct addressing mode
Mod
Reg
R/M
2
3
3

## Slide 80: The ModR/M Byte – II
The Reg field specifies the register operand (if necessary)
The Mod and R/M bits determine the format of the memory operand (if it exists)
If R/M = 100 , we get the scale index and base from the subsequent SIB byte

## Slide 81: Scale Index Base
There are four values of the scale : 00 (1), 01 (2), 10 (4), 11 (8)
Both the index and base are 3 bits each, and follow the register encoding scheme
Some rules :
  esp cannot be an index
  The offset in the memory address can only be specified in the displacement field
Scale
2
3
3
Index
Base

## Slide 82
Register Encoding
Code | Register
000 | eax
001 | ecx
010 | edx
011 | ebx
100 | esp
101 | ebp
110 | esi
111 | edi
** If the R/M bits are 100 , then we use the SIB byte
** If Mod = 00, and R/M = 101 (ebp), we use memory direct addressing The 32 bit displacement is used as the memory address

## Slide 83
Example
Encode the instruction: add ebx, [edx + ecx*2 + 32]. Assume that the opcode
for the add instruction is 0x03.
Answer:
Let us calculate the value of the ModR/M byte. In this case, our displacement fits within 8 bits. Hence, we can set the Mod bits equal to 01 (corresponding to an 8 bit displacement). We need to use the SIB byte because we have a scale and an index. Thus, we set the R/M bits to 100. The destination register is ebx. Its code is 011. Thus, the ModR/M byte is : 01 011 100 (0x5C)
Now, let us calculate the value of the SIB byte. The scale is equal to 2 (01). The index is ecx(001), and the base is edx (010). Hence, the SIB byte is: 01 001 010 = 0x4A.
The last byte is the displacement, which is equal to 0x20.
Thus, the encoding of the instruction is : 03 5C 4A 20 (in hex)

## Slide 84
THE END