## Slide 1
Chapter 12
I/O and Storage Devices
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
Smruti Ranjan Sarangi, IIT Delhi
Computer Organisation and Architecture
PowerPoint Slides
PROPRIETARY MATERIAL. © 2014 The McGraw-Hill Companies, Inc. All rights reserved. No part of this PowerPoint slide may be displayed, reproduced or distributed in any form or by any means, without the prior written permission of the publisher, or used beyond the limited distribution to teachers and educators permitted by McGraw-Hill for their individual course preparation. PowerPoint Slides are being provided only to authorized professors and instructors for use in preparing for classes using the affiliated textbook. No other use or distribution of this PowerPoint slide is permitted. The PowerPoint slide may not be sold and may not be distributed or be used by any student or any other third party. No part of the slide may be reproduced, displayed or distributed in any form or by any means, electronic or otherwise, without the prior written permission of McGraw Hill Education (India) Private Limited.
1

## Slide 2
These slides are meant to be used along with the book: Computer Organisation and Architecture, Smruti Ranjan Sarangi, McGrawHill 2015
Visit: http://www.cse.iitd.ernet.in/~srsarangi/archbooksoft.html

## Slide 3: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 4: I/O Devices
Computer
Memory
Hard disk
Keyboard
Mouse
Monitor
Printer

## Slide 5: I/O Devices
I/O Devices
  Hard disk
  Network card
  Printer, scanner, camera, speakers
They are connected to the motherboard with I/O ports
  A set of metallic pins for attaching with external connectors
  Example : USB port, DVI Port.

## Slide 6: Software's View of I/O Devices
Linux defines two system calls
  read (int file_descriptor, void *buffer, int num_bytes)
  write (int file_descriptor, void *buffer, int num_bytes)
All devices are perceived to be files in the /dev file system
  We can read bytes from them, or write bytes to them
  Two kinds of devices : character (keyboard, mouse), and block (hard disk, network card)

## Slide 7: Operating System's I/O Stack
A request goes through the kernel, device driver, processor, and I/O system
I/O devices are connected to the motherboard via add-on cards, or directly
Application
Operating
system
Kernel
Device
driver
Processor
I/O
system
I/O
device
Software
Hardware
Request
Response

## Slide 8: A Network Card

## Slide 9: Chipset and Motherboard
A motherboard is a printed circuit board connecting the processors and auxiliary chips
The additional chips comprise the chipset

## Slide 10: Architecture of the Motherboard
Processor
North Bridge
chip
Frontside
bus
Graphics
processor
Memory
modules
PCI express
bus
South Bridge
chip
Hard
disk
SATA
bus
Network
card
PCI express
bus
USB
USB
USB
USB
USB ports
Audio/ Mic
ports
PCI express
bus
Intel high
def. audio on
a PCI bus

## Slide 11: I/O Buses
The different components on the motherboard are connected with I/O buses
I/O buses are also used to connect external devices to the motherboard
An I/O bus is a set of wires that carries data and control signals between a set of devices. These devices use the bus to transmit data and control signals between each other.

## Slide 12: Layers in the I/O System
Physical layer
Transmission
Synchronisation
Data link layer
Network layer
Protocol layer

## Slide 13: Layers in the I/O System
Physical Layer
  Transmission Sublayer → Defines the electrical specifications of the bus, and the methods for encoding data
  Synchronisation Sublayer → The timing of signals
Data link layer
  Framing, buffering, error correction, transactions

## Slide 14: Layers - II
Network Layer
  I/O device addressing, location, routing
Protocol Layer
  End to end request processing
  Interrupts, and polling
  DMA (Direct Memory Access)

## Slide 15: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 16: Active High and Active Low
Clock
Data
1
0
1
1
0
1
0
1
0
0
0
(a) Active high signalling
Clock
Data
1
0
1
1
0
1
0
1
0
0
0
(b) Active low signalling

## Slide 17: LVDS Signalling
If (A = 1) there is a voltage difference of 350 mV across the op Amp
Else there is a voltage difference of -350 mV
Smaller is the voltage swing, faster is the circuit
V
cc
3.5mA
A
A
A
A
+
-
Op amp
100 Ω
line 1
line 2
T1
T2
R
d
Low Voltage Differential Signalling

## Slide 18: Terminology
Physical Bit
  A value of 0 or 1 on the bus
Logical Bit
  A function of a sequence of physical bits. Logical bits are passed to the next layer.
Bit Period
  Time it takes to transmit a single bit
I/O Clock Period
  One clock cycle of the I/O clock

## Slide 19: Binary vs Ternary Signalling
Binary Signalling → The physical bit can either take a value of 0 or 1
Ternary Signalling → We have three physical bits : 0, 1, and idle
  The idle state of the bus corresponds to the case where no signal is transmitted
  LVDS naturally supports ternary signalling. When the voltage difference is less than the threshold, the bus is in the idle state.

## Slide 20: Return to Zero (RZ)
Logical 0 : 0 → idle
Logical 1 : 1 → idle
Clock
Data
1
0
1
1
0
1
0
1
0
0
0

## Slide 21: Manchester Encoding
Logical 1 : 0 → 1
Logical 0 : 1 → 0
Clock
Data
1
0
1
1
0
1
0
1
0
0
0

## Slide 22: Non Return to Zero (NRZ)
Logical 0 : physical 0
Logical 1 : physical 1
Clock
Data
1
0
1
1
0
1
0
1
0
0
0

## Slide 23: Non Return to Zero Inverted (NRZI)
Logical 0 : no transition
Logical 1 : transition
Clock
Data
1
0
1
1
0
1
0
1
0
0
0

## Slide 24: Synchronisation Sublayer
How does the receiver know, when to read the data ?
  It might not have the same clock as the sender
  The signal might have a variable amount of delay
  The receiver might sample the clock in the keepout region
    The signal cannot be sampled in a certain interval of time around the clock edge (recall setup time, and hold time)

## Slide 25: Synchronous Buses
Sender and receiver have the same clock
The signal arrives at the receiver before its clock enters the keepout region
Figure shows the receiver circuit
D
Q
I/O link

## Slide 26: Mesochronous Buses
Fixed (known) propagation delay
Use a delay element to keep transitions out of the keepout region
D
Q
I/O Link
Tunable delay
element

## Slide 27: Source Synchronous Bus
Sender sends clock along with the signal
Clock data in with the sender's clock (xclk)
Transfer the data to the receiver's clock domain using a tunable delay element
D
Q
I/O link
Tunable delay
element
Delay calculator
xclk
D
Q
rclk
to receiver
rclk

## Slide 28: Asynchronous Bus
No guarantee of timing
Recover the clock from the transitions in the data
Transfer to the receiver's clock domain using a delay element
D
Q
I/O Link
Tunable delay
element
Delay calculator
D
Q
rclk
to receiver
rclk
Clock recovery
circuit

## Slide 29: Communication with Strobe Signals
The strobe signal indicates the availability of data.
The sender has no way of knowing that the receiver has read the data
Strobe
Data

## Slide 30: 4 Phase Handshake
Receiver asserts the ack signal after it has read data.
The sender deasserts the strobe, and stops sending data
The receiver resets the ack signal
Strobe
Data
Ack

## Slide 31: 2 Phase Handshake
Instead of asserting, and deasserting signals, we toggle their values
No need to pause between transmtting bits.
The sender starts sending the next bit after it sees the ack line to be toggled
Strobe
Data
Ack

## Slide 32: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 33: Framing
Create a frame of data from logical bits
A frame is an atomic unit of data (data packet)
How do we detect frames ?
  Demarcation by inserting pauses → wastes bandwidth
  Bit count → Count the number of bits. What if we miss a bit ?

## Slide 34
Frame Detection
  Bit/Byte Stuffing → Insert special symbols at the beginning and end of frames.
  For example, insert the sequence : 0xDEADBEEE, at the beginning. If DEADBEEE occurs inside the message, repeat the symbol two times. (Similar to ‘\’ in C++/ Java)

## Slide 35: Error Detection/ Correction
Single error detection. Have a parity bit.
Data bits
Parity bit
....

## Slide 36: Other Error Detection/Correction Schemes
Single Bit Error Correction → Achieved by having multiple parity bits (taught in classes on data communication, and coding theory)
SECDED (Single Error Correct, Double Error Detect) →Taught in courses on coding theory
CRC (Cyclic redundancy check) → Used to check a burst of errors.

## Slide 37: Arbitration
In a multidrop bus, multiple transmitters are connected to a single bus
How do they get access to the bus ? Use a method called arbitration
Two methods for arbitration → centralised, and daisy chain

## Slide 38: Centralised Arbitration
request → grant → release
Arbiter
Device 1
Device 2
Device 3
Device 4
Request
Grant
Release
Request
Grant
Release
R
e
q
u
e
s
t
G
r
a
n
t
R
e
l
e
a
s
e
G
r
a
n
t
Request
Release

## Slide 39: Daisy Chain Arbitration
Device interested to transmit asserts bus grant
The arbiter injects a token.
The token passes from device to device.
The last device sets the release signal, and destroys the token.
Arbiter
Device 1
Device 2
Device n
Bus grant
Bus release

## Slide 40: Transaction Oriented Bus
A request from the sender to the receiver has a given semantics. It consists of an atomic sequence of messages.
This is called a transaction.
Bus that allows both sides to communicate at the same time → full duplex
Only one side at a time → half duplex

## Slide 41: DRAM Read Transaction
clock
RAS
CAS
Address
Command
Data ready
Data
row
read
read
col
row
col

## Slide 42: Split Transaction Buses
A transaction unnecessarily ties up the bus
A transaction might also have long pauses in the middle.
Use a split transaction bus. Typically consists of a request sub-transaction, and response sub-transaction.
Other messages can be sent between request and response.
Flexible, increases bandwidth, simpler

## Slide 43: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 44: I/O Port Addressing
Every device on the motherboard exposes a set of I/O ports.
  An I/O port in this case, is a software entity.
  Each software I/O port is a wrapper on the actual hardware I/O port
Port connector
Port controller
Registers
Input
Output
Software interface

## Slide 45: Software Interface
Each I/O port exposes a set of 8-32 bit registers to software
Software writes to the registers. The port controller automatically sends the information to the I/O device.
Similarly, to read data the processor reads the registers of the port controller.
Example : Intel processors define 64K, 8 bit I/O ports. Each port has a 16 bit port number.

## Slide 46: I/O Address Space
Set of all I/O ports that are accessible to software
x86 processors have two instructions to access I/O ports → in and out
Instruction
Semantics
In r1,<io port>
r1 ←
Contents of <i/o port>
Out r1, <io port>
Contents of <i/o port> ←
r1

## Slide 47: I/O Mapped I/O
A request contains an I/O port address
The processor sends it to the Northbridge chip.
The Northbridge chip forwards it to the Southbridge chip (if necessary)
The Southbridge chip forwards it to the destination. (there might be several more hops)
Each chip maintains a small routing table.
The response follows the reverse path.

## Slide 48: Memory Mapped I/O
Problems with I/O mapped I/O
  The programmer needs to be aware of the addresses of the I/O ports.
  The same device might have different port addresses across different motherboards
  Programs will cease to work.
  It is hard to transfer a block of data (need to send it instruction by instruction)
  Solution : memory mapped I/O

## Slide 49: Memory Mapped I/O
Define a virtual layer between I/O ports, and the application.
The operating system can use the paging mechanism to map I/O ports to memory addresses.
Whenever, we write to a memory address that is mapped to an I/O port, the TLB directs the request to the I/O system.
Similarly, for reading data, the response comes from the I/O System

## Slide 50: Advantages
The operating system creates the mapping between the I/O ports and the memory addresses
The same I/O program runs on multiple machines
Reading and writing to I/O devices requires normal load/store instructions
Easy to read and write a large block of data using block load/store operations available in some architectures (e.g, x86)

## Slide 51: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 52: Protocol Layer
Defines the interaction between the host (processor) and I/O devices
The protocol layer consists of high level commands that are sent over the three lower layers
Three methods :
  (1) Polling, (2) Interrupts, (3) DMA (Direct Memory Access)

## Slide 53: Polling
Example :
  Assume that the application running on the processor wants to print a page.
  It needs to first find if the printer is free before sending it the contents of the page.
  It keeps querying the printer for its status. If its status is busy, the program waits for some time, and queries again.
  This method is known as polling.
  Simple, yet inefficient (traffic, power, computational time)

## Slide 54: Interrupts
The host tells the device to notify it if there is a change in its status
In this case, if the printer is busy, then the host lets the printer know that it is interested in printing one more page.
The printer sends it an interrupt, once it is free.
The host processes the interrupt, and the application subsequently sends the print job

## Slide 55: DMA (Direct Memory Access)
Now, let us assume that the application is aware that the printer is free.
It needs to transfer several MB of data to the printer for printing.
  If it transfers data byte by byte, the processor will be tied up for the entire duration
  Even if it uses memory mapped I/O, the entire operation will require a large amount of CPU time.
  Best solution : outsourcing

## Slide 56: DMA Engine
Assign the work of transferring data between main memory and the I/O devices to the DMA engine
  The DMA (direct memory access) unit is typically a part of the Northbridge chip
  It has access to main memory, and to I/O devices. It can seamlessly transfer data between them.
  Once it is done, it sends an interrupt to the processor.
  The processor programs the DMA engine with the addresses in memory, size of data, and I/O address locations

## Slide 57: DMA Modes
Burst mode
  Locks the FSB and the buses to the I/O device till the entire transaction is over.
Cycle stealing mode
  Split-transactions
  Transfers data in smaller chunks. DMA traffic typically has a much lower priority than regular traffic.

## Slide 58: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 59: PCI Express
Motherboards needs a bus to connect the I/O elements
  There were many buses in use in the late nineties. Two of them were very popular.
    PCI (Peripheral Component Interconnect)
    AGP (Accelerated Graphics Port)
A standardisation effort led to the PCI-Express (PCI-X) bus
A PCI Lane is a :
  High speed serial bus.
  Does not use parallel links because of the possibility of different amounts of delay across the links. Synchronisation across links is difficult.

## Slide 60
PCI Express (Peripheral Component Interconnect Express)
Usage
As a mother board bus
Specification
PCI Express specifications (link)
Topology
Connection
Point to point with multiple lanes
Lane
A single bit full duplex channel with data striping
Number of Lanes
1 to 32
Physical Layer
Signalling
LVDS based differential signalling
Encoding
8 bit/10 bit
Timing
Source synchronous
Data Link Layer
Frame Size
1byte
Error Correction
32 bit CRC
Transactions
Split transaction bus
Bandwidth
250 MB/s per lane
Network Layer
Routing Nodes
Switches

## Slide 61: USB
USB (Universal Serial Bus)
  De facto standard for connecting all types of peripherals to a computer (as of today)
  Scanners, printers, cell phones, pen drives, …
This is also a serial bus to allow high speed signalling.
Each USB port (host) can be connected to a set of devices arranged as a tree.
  Each internal node is known as a hub
  We can connect a total of 127 devices (including hubs). max depth = 5

## Slide 62: USB Physical Layer
A USB connector has 4 pins
  Vcc → 5V DC
  D+ and D- : differential pair (3.3V)
  Gnd pin
  Micro and Mini USB ports have an additional pin → ID (helps differentiate between device and host)
Uses NRZI signalling with dummy bits (for clock recovery)

## Slide 63: USB Data Link Layer
Four kinds of packets
  Control → control messages to configure devices
  Interrupt → interrupts
  Bulk → Large amount of data transfer (printing a page)
  Isochronous → Data transfer at a fixed rate (web camera)
Implements a split transaction bus

## Slide 64: Network Layer
Each USB device is assigned a 7 bit id by the host
  Every USB device defines a set of I/O ports, limited to
    16 IN ports
    16 OUT ports
  Thus each port has a unique 11 bit address
  Software drivers talk to the device by sending messages to the corresponding port.
Protocol Layer
  Stream pipe (unstructured), message pipe (structured with a handshaking mechanism)

## Slide 65: USB Summary
USB (Universal Serial Bus) | 
Usage | Connecting peripheral devices  keyboards, mice, web cameras, pen drives
Topology | 
Connection | Point-to-point, Serial
Width | Single bit, half-duplex
Physical Layer | 
Signalling | LVDS based differential signalling
Encoding | NRZI (transition represents a logical 0)
Timing | Asynchronous (a 0 added after 6 continuous 1s for clock recovery)

## Slide 66
USB Summary - II
Data Link Layer | 
Frame Size | 46 – 1058 bits
Error Correction | CRC
Transactions | Split Transaction Bus
Bandwidth | 192 KB/s (low speed) 1.5 MB/s (full speed) 60 MB/s (high speed)
Network Layer | 
Address | 7 bit device id, 4 bit end point id
Routing | Using a tree of hubs
Hub | 1 upstream port, up to 4 downstream ports
USB Network | Can support a maximum of 127 devices
Protocol Layer | 
Connections | Message Pipe (structured), and stream pipe (unstructured)
Type of Traffic | Control, Interrupt, Bulk, Isochronous

## Slide 67: Outline
Overview
Physical Layer
Data Link Layer
Network Layer
Protocol Layer
Case Studies
Storage Media

## Slide 68
Hard Disks
Optical Drives
Solid State Drives

## Slide 69
Hard Disks

## Slide 70: Data Storage in Hard Disks
Magnetic storage (sequence of tiny magnets)
NRZI Encoding
  with dummy bits
N
S
N
S
N
S
N
S
N
S
0
1
0
1

## Slide 71: Structure of a Platter
A platter is divided into concentric rings (track)
Each track is divided into fixed size sectors
Track
Sector

## Slide 72: Structure of a Hard Disk

## Slide 73: Structure in Detail
Platter
Spindle
Spindle motor
Read/Write
head
Arm
Actuator
Drive
electronics
Bus
interface
Bus

## Slide 74: Accessing a Given Sector
Position the head on the correct track
  seek time
Wait for the desired sector to come under the head
  Rotational Latency
  Assume that the hard disk rotates at constant angular velocity
Read or Write data
  Perform error checking, correction, framing
  Transfer data to the CPU → (Transfer Time)
  The transfer starts when the head is on the first bit of the sector

## Slide 75: Logical vs Physical Block Address
Software programs use the logical block address to address a hard disk block (sector)
  The hard disk internally converts the logical address to a physical address (recording surface, track, sector)
  It dedicates a recording surface for storing this information.
  It has a small cache (DRAM) to store the most recently used mappings
  The hard disk can also use this mechanism to mark bad sectors and remap logical sectors to healthy physical sectors.

## Slide 76
RAID – (Redundant Array of Disks)
Hard Disks tend to have high failure rates
  Too many mechanical components
  High temperature sensitivity
What do we do?
  Do we lose all our data ....
  NO
Use RAID
  Redundant disks
  To tolerate faults, and recover from failures

## Slide 77
RAID – II
What about bandwidth?
  Assume we want to read two different blocks from the same disk?
  We need to read them serially.
  Low Bandwidth
How can we increase bandwidth
  Read from multiple disks in parallel.
  Solution: RAID

## Slide 78
B9
B7
B5
B3
RAID 0
B1
B10
B8
B6
B4
B2
Disk 1
Disk 2
No Reliability
Allows us to read even and odd blocks in parallel
Block 1
(512 bytes)
Distributing data across disks defined as data striping

## Slide 79
B5
B4
B3
B2
RAID 1
B1
B5
B4
B3
B2
B1
Disk 1
Disk 2
Immune to one disk failure
Can read blocks B1 and B2 in parallel
100% overhead in storage

## Slide 80
B17
B13
B9
B5
RAID 2, 3, 4
B1
Disk 1
Immune to one disk failure
Parity block  P1 =
25% storage overhead
If a disk fails, add a new disk and reconstruct it from the parity bits
B18
B14
B10
B6
B2
Disk 2
B19
B15
B11
B7
B3
Disk 3
B20
B16
B12
B8
B4
Disk 4
P5
P4
P3
P2
P1
Parity Disk

## Slide 81
B17
B13
B9
B5
RAID 2, 3, 4
B1
Disk 1
B18
B14
B10
B6
B2
Disk 2
B19
B15
B11
B7
B3
Disk 3
B20
B16
B12
B8
B4
Disk 4
P5
P4
P3
P2
P1
Parity Disk
RAID | Block Size
2 | 1 bit
3 | 1 byte
4 | 1 block (512 bytes)
Single point of contention
For reading a single block  access all the disks

## Slide 82
B17
B13
B9
P2
RAID 5
B1
Disk 1
To avoid this problem: Distribute the parity blocks across the disks
Reliable + high bandwidth
B18
B14
P3
B5
B2
Disk 2
B19
P4
B10
B6
B3
Disk 3
P5
B15
B11
B7
B4
Disk 4
B20
B16
B12
B8
P1
Disk 5

## Slide 83
B17
B13
P3A
P2B
RAID 6
B1
Disk 1
Immune to two disk failures
Have two parity blocks (parity is computed differently)
High reliability at the cost of increased storage overhead
B18
P4A
P3B
B5
B2
Disk 2
P5A
P4B
B9
B6
B3
Disk 3
P5B
B14
B10
B7
B4
Disk 4
B19
B15
B11
B8
P1A
Disk 5
B20
B16
B12
P2A
P1B
Disk 6

## Slide 84
Optical Drives
CD
DVD
Blu-Ray

## Slide 85
Structure of an Optical Disc
Polycarbonate layer
Reflective Layer
Plastic/ Surface Layer
Lacquer Layer
Laser
Land
Pit

## Slide 86
Physical bits:
  Lands represent the physical bit 1
  Pits represent the physical bit 0
Logical bits
  Encoded using the NRZI encryption scheme
Elaborate error protection codes
Encoding Data

## Slide 87
Design of an Optical Drive

## Slide 88: Operation of the Optical Disc Drive
Rotates at constant linear velocity
   linear velocity
   angular velocity
  r  radius
The motor changes its speed (rpm) depending on the position of the head
It analyses the reflected light and figures out the sequences of bits (NRZI scheme)

## Slide 89: Technology Generations
 | CD | DVD | Blu-Ray
Generation | 1st | 2nd | 3rd
Capacity | 700 MB | 4.7 GB | 25 GB
Uses | Audio | Video | High Def. Video
Laser wavelength | 780 nm | 650 nm | 405 nm
Raw 1X transfer rate | 153 KB/s | 1.39 MB/s | 4.5 MB/s

## Slide 90
Solid State Drives

## Slide 91: Floating Gate (FG) Transistor
The FG transistor has 2 gates – control gate and floating gate
When we apply a very high voltage to the control gate
  Electrons get deposited in the floating gate
  Increases the threshold voltage of the transistor
  The FG transistor is said to be programmed (value = 0)
  Not programmed (value = 1)
Source
Drain
SiO
2
Floating gate
Control gate
Symbol
(a)
(b)

## Slide 92: Reading the Value in a FG Transistor
Depositing electrons increases the threshold voltage
  Increases from to ( > )
  When the cell contains a logical 1 
  When the cell contains a logical 0 
Set the gate voltage to a value between a
  If a cell has 1, it will conduct
  Otherwise, it will not conduct

## Slide 93: NOR Flash
Rarely used → low density, low bandwidth, faster
Read the value of the bit line using a sense amplifier
Operation  Similar to a DRAM array (see Chapter 6)
WL1
WL2
Bit
line

## Slide 94: NAND Flash
To read a certain transistor, enable the rest of the transistors and ground select and bit line select
High density
40-60% more density than NOR flash
Bit line
select
WL4
WL3
WL2
WL1
WL8
WL7
WL6
WL5
Ground
select
Bit line

## Slide 95: Blocks and Pages
A page contains 512-4096 bytes of data
  Most NAND flash devices read/write data at the granularity of pages
  Has additional bits for error correction (CRC)
Blocks contain 32-128 pages
  Size: 16 to 512 KB
  Can erase data at the level of blocks (deprogram)
Program Erase Cycle
  To rewrite a page, we need to erase it first
  Converting 0s to 1s (deprogramming) is slow and has to be done at large granularities

## Slide 96: Wear Levelling
Flash memory can only tolerate a certain number (100k) of program/erase cycles (P/E)
  The SiO2 layer breaks down and does not remain an insulator, hence the device cannot hold charge anymore
  Solution :
    Keep counters for each block
    Increment the counter on each P/E cycle
    Aim: Ensure that the number of P/E cycles for each block is roughly the same.

## Slide 97: Wear Levelling and Read Disturbance
Wear Levelling
  Once a counter reaches a high value.
  Swap the contents of a frequently accessed block with a less frequently accessed block
  Keep a high level mapping table:
    Logical block number  Physical block location
    Just change the mapping in this table
Read disturbance
  It is possible that repeatedly reading a transistor causes the contents of the rest of the transistors to change
  Same approach: have a counter, copy the block to another location, if the counter exceeds a threshold.

## Slide 98
THE END